## Slide 1: WATER ALLOCATION TOOL
AKA DWRAT, pyWRAT, etc.

## Slide 2: OUTLINE
Intro / Background to DWRAT, pyWRAT, etc.
Optimization Problems
Allocation Tool Overview
Formulations
Example Basin
Discussion / Q & A
    New name?
Calculations / Programming
    Vectorization
    Numerical Python

## Slide 3: MOTIVATION
A need for a formal procedure and tools to evaluate water availability that are:
  Quantitative
  Transparent
  Open source
  Easy to learn
  Inexpensive to implement

## Slide 5: OPTIMIZATION PROBLEMS
Resource Allocation
Facility location decisions
Supply chain management
Blending problems

## Slide 6: OPTIMIZATION PROBLEMS
HAVE THREE KEY COMPONENTS:
An objective function we want to optimize
A set of decision variables or allocations that need to be set to find the optimum of the objective function
A set of constraints that restrict the values of the variables

## Slide 7: KNAPSACK PROBLEM

## Slide 8: EXAMPLE OPTIMIZATION PROBLEM
What is the minimum cost to enclose a 400 sq-ft garden if Sam’s neighbor is paying half of the shared side?
https://www.matheno.com/calculus-1/optimization/garden-fence/

## Slide 9: DECISION VARIABLES
Dimensions of garden:
  x (width)
  y (length)

## Slide 10: CONSTRAINT
A (area) = 400 square feet
A = x*y = 400
Solve or y in terms of x:
y = 400 / x

## Slide 11: OBJECTIVE FUNCTION
Minimize C, (cost)
As a function
of x:

## Slide 12: SOLVE

## Slide 13: SOLVE (continued)

## Slide 14: SOLVE (continued)

## Slide 15: MS EXCEL SOLVER add-in

## Slide 16: PuLP 2.0
Open source Python package for Linear Program modeling
  Integrates with many available solvers
  Used by UC Davis in both DWRAT and pyWRAT
Able to handle 1000s of decision variables vs. MS Excel maximum of 200
  (Every watershed has one decision variable per sub-basin, and one per appropriative user)

## Slide 18: WATER ALLOCATION TOOL
DWRAT
  Implemented as Linear Program in Excel with OpenSolver (free) solution engine
pyWRAT
  Implemented in Python using PuLP solver and Pandas data analysis packages
pyWRAT 2.0 (?)
  Vectorized, implemented in Python using PuLP solver and Numerical Python (numpy) packages

## Slide 19: ASSUMPTIONS
Every user has access to all basin flow, i.e. every user can divert from the outlet
All water use is 100% consumptive – no return flows
No losses to groundwater or evaporation
Flow is available to the whole network at each time step

## Slide 20: VARIABLE DEFINITIONS
i : user subscript
k : basin subscript
Pk : basin proportion
Ai : user allocation
ui : user demand
vk : basin inflow
ek : environmental flow
wk : basin downstream cost
pi : appropriative user priority

## Slide 21: OPTIMIZATION PROBLEMS
HAVE THREE KEY COMPONENTS:
An objective function we want to optimize
A set of decision variables or allocations that need to be set to find the optimum of the objective function
A set of constraints that restrict the values of the variables

## Slide 22: RIPARIAN DECISION VARIABLES
Basin proportions of demand allocated to riparian users:
Actual allocation is determined by proportions

## Slide 23: APPROPRIATIVE DECISION VARIABLES
Actual allocation for each appropriative user

## Slide 24: MASS BALANCE CONSTRAINTS
RIPARIAN
APPROPRIATIVE

## Slide 25: WATER RIGHTS RULES (CONSTRAINTS)
Riparian Rights
Have highest priority
Share shortages proportionally
Appropriative Rights
First in time, first in right

## Slide 26: RIPARIAN LEGAL CONSTRAINTS
Shared shortage:
However:

## Slide 27: APPROPRIATIVE LEGAL CONSTRAINTS
Seniority system shortage is minimized according to seniority:
Shortage is scaled in the objective function by the inverse of the priority aka (shortage penalty)

## Slide 28: RIPARIAN OBJECTIVE FUNCTION
Maximize riparian allocations:

## Slide 29: APPROPRIATIVE OBJECTIVE FUNCTION
Maximize appropriative allocations by seniority:

## Slide 31: EXAMPLE
From Drought Water Right Curtailment Analysis for California’s Eel River.
Lord et al. - Journal of Water Resources Planning and Management - 2018

## Slide 32: BASIN DATASETS

## Slide 33: USER DATASETS

## Slide 34: RIPARIAN ALLOCATIONS
From Water rights curtailments for drought in California: Method and Eel River Application
Benjamin Lord’s Master Thesis 2015

## Slide 35: APPRIOPRIATIVE USER ALLOCATIONS

## Slide 36: QUESTIONS ?

## Slide 37: CALCULATIONS, PROGRAMMING APPROACHES, NUMERICAL PYTHON, ETC.

## Slide 38: EXAMPLE CALCULATION
for all i users, in each basin k
  We need to multiply each user’s demand by basin proportion
  But we need to specify location of each user with a matrix

## Slide 39: MATRIX OPERATIONS

## Slide 40: VECTORIZATION
The process of converting routines that sequentially loop over elements to matrix operations
Vectorized operations are several orders of magnitudes faster,
And easier to understand from a mathematical perspective

## Slide 41
NESTED FOR LOOPS
MATRIX OPERATION
X ∙ Y
Or might need the
transpose:
XT ∙ Y
For all i,
  For all j,
    sum (Xi * Yj)

## Slide 42: MATRIX MULTIPLICATION

## Slide 43: MATRIX TRANSPOSITON

## Slide 44: UPSTREAM CALCULATION
Basin Demand is the sum of user demand upstream of each basin k x i user connectivity matrix * i x 1 list of user demand = k x 1 basin demand
=
∙

## Slide 45: CONNECTIVITY MATRIX - BASINS
A value of 1 indicates row subbasin flows to corresponding column subbasin

## Slide 46: CONNECTIVITY MATRIX - USERS
A value of 1 indicates user (column) is upstream of basin outlet (row)
Used for implementation of mass balance constraints
Generated with GIS in larger river basins
 |  | Users |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Basins | A |  |  |  | 1 |  |  |  |  |  |  | 1
 | B |  |  | 1 |  |  |  |  |  |  |  | 
 | C |  | 1 | 1 | 1 |  |  |  |  |  |  | 1
 | D |  |  |  |  |  |  | 1 |  |  |  | 
 | E |  | 1 | 1 | 1 |  | 1 | 1 | 1 |  |  | 1
 | F | 1 | 1 | 1 | 1 |  | 1 | 1 | 1 |  | 1 | 1
 | G |  |  |  |  |  |  |  |  | 1 |  | 
 | H | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 47: NUMERICAL PYTHON (NUMPY)
provides fast and efficient operations on arrays of homogeneous data.
NumPy extends python into a high-level language for manipulating numerical data, similar to MATLAB.
Most operations are one line of code, and very readable mathematically
Example: user allocation
user_allocation_list = (numpy.matmul (basin_proportions_list.transpose(), basin_user_matrix) * demand_data)

## Slide 48: QUESTIONS ?

## Slide 49: ALTERNATIVE ALLOCATION APPROACHES